## Slide 1: 2019 First Nation Launch – Oral Presentation
UCLA Bearospace

## Slide 2: Team Information
School: University of California, Los Angeles
Team Name: UCLA Bearospace
Mentor: Frank Nobile
Advisor: Dr. Audrey Pool O’Neal
Presenting Members: Lucia Gonzalez Ryan Rio
Sophia Martinez Rossana Rico
Aidan Carrizales Gisselle Livingston
Joshua Diaz Javier Gomez
Andy Muratalla Achille Hebert

## Slide 3: Launch Vehicle
Carbon Fiber Upper & Lower Body Tube
  Length - 26’’
  ID - 3.879’’
  Thickness - 0.038’’
PLA/ABS Nose Cone
  Length - 13’’
  Shoulder Length - 3.879’’
  Thickness - 0.222’’
Pine Nose Cone Bulkhead
  Small Diameter - 1.772’’
  Large Diameter - 1.972’’
  Thickness - 0.7320’’
Pine Bulkhead
  OD - 3.879’’
  Thickness - 0.748’’
Pine Centering Rings
  Outer Diameter (OD)
    W/ Rods - 3.8475’’
    Bottom - 3.8495’’
  Inner Diameter (ID)
    W/ Rods - 2.2945’’
    Bottom - 2.275’’
  Thickness -
    W/ Rods - 0.761’’
    Bottom - 0.7585
Carbon Fiber Coupler
  Length - 7.8’’
  OD - 3.879’’
Pine Fin Securing Mechanism
  OD - 3.8395’’
  Thickness - 0.7610’’
  Slots - 0.1545” x 0.46”
Pine Custom Locking Mechanism
  OD - 3.8470’’
  Thickness - 1.6’’
Fiberglass Fins
  Thickness - 0.134’’
3 Threaded Rods
  Total Mass - 20.99 oz
Total Length
  65.915’’
Avionics Storage Section w/ locking mechanism
  ~12.5 inches
Final Motor Choice
  54mm Aerotech J450DM

## Slide 4: Launch Vehicle Performance
Stability: 1.12 cal
CP: 47.707 in*
CG: 43.288 in*
Thrust to Weight Ratio**: 10.550
Rail Exit Velocity ***: 57.9 ft/s
Time To Apogee: 15 s
Predicted Apogee: 1445ft
*Measured from tip of nosecone
**Average thrust of propellant vs total weight of rocket
*** 72” Rail
Flight Profile: Altitude, Velocity, Acceleration

## Slide 5: Avionics Subsystem
Electronics Bay
  12.5’’ x ø3.9’’ designated space
  10.9’’ sled
  Located 21’’ from the nose cone
Vent Holes
  Four ø0.174’’ vent holes will be drilled 6’’ from the locking mechanism
Component | Power | Switch
Missile Works RRC3 | 9 V battery | Switches will be connected externally and will be hooked up to switch ports in altimeters.
PerfectFlite Stratologger SL100 | 9 V battery | 
Arduino Uno | 9 V battery | Switch will be wired in series with ground since there is no dedicated switch in the Arduino Uno. Switch will also be connected externally.
MPU6050 |  | 
BMP180 |  | 

## Slide 6: Recovery Subsystem
Parachute Recovery Scheme
  Drogue Chute: 21.5 inch diameter, deployed at apogee, located between lower and upper body tubes
  Main Chute: 60 inch diameter, deployed at 500 feet agl, located between upper body tube and nose cone.
Descent Rate
  Descent Rate Post-Drogue Chute deployment: 63.5 ft/s.
  Descent Rate Post-Main Chute deployment: 21.2 ft/s.
  Total Descent Time: 79.1 seconds
  Impact Velocity: 21.2 feet/second
Tracking Devices
  None on-board
  Will rely on visual of rocket
Ejection Charges
  2 Black Powder Charges
  1 Motor Ejection Charge
Main Chute
Drogue Chute
Shock Cords
Nose Cone
Eye bolts drilled into centering rings and bulkheads
Quick links used to attach shock cords to eye bolts
Upper Body Tube
Lower Body Tube

## Slide 7: Payload / Experiment
Components
  Arduino Uno (microcontroller
  MPU6050 (gyroscope/accelerometer)
  BMP180 (barometric pressure sensor)
  Micro SD Card module
  9V Battery
Nestled into Avionics sled
Records 5 data types (acceleration, gyration, pressure, temperature, and altitude) and saves them onto a microSD card
Arduino is powered by a 9V battery, which powers the rest of the electronics
  Once switch is connected, Arduino will initialize a calibration phase which will calibrate the gyroscope
  Pressure and altitude must be manually calibrated by inputting pressure conditions for the day
  Data is stored in a microSD card. Each data type is delineated by a comma “,“

## Slide 8: Challenges / Lessons Learned
Technical Challenges
  Balancing mass components for an acceptable stability
  Accessibility of machinery needed to manufacture parts
  Calibration of various sensors
Programmatic Challenges
  Acquiring necessary parts in a reasonable time frame
  Creating a fast-paced yet unrushed schedule of events
Lessons Learned
  Keep an updated OpenRocket file available to all members during build phase
  Always have a back up plan for machining
  Thoroughly research all sensors before use
  Order parts as soon as need arises
  Planning more sequential workshops for new members

## Slide 9: Questions?