## Slide 1: First Nations Launch 2023 Avionics Webinar
The material contained in this document is based upon work supported by a National Aeronautics and Space Administration (NASA) grant or cooperative agreement. Any opinions, findings, conclusions or recommendations expressed in this material are those of the author and do not necessarily reflect the views of NASA.
Aaron Ashley, System Safety Engineer, Raytheon Missiles & Defense
January 17, 2023

## Slide 2: Webinar Overview
COTS Altimeters
Switches
Power
Tracking
Avionics Hardware

## Slide 3: Avionics
The term ‘avionics’ is used to describe all electronic components that control the flight of the vehicle
  This typically includes altimeters and tracking
  This does not include any ‘payload / challenge’ components
    These do not affect the flight of the vehicle
    The vehicle should be designed to still have a successful flight without the payload
Although sometimes used synonymously, the term payload is not the same as the term avionics

## Slide 4: COTS Altimeter
COTS means a Commercial Off-The-Shelf device
  You cannot fabricate/program your own altimeter for ejection events
Altimeters are a small electronic device
  Barometric pressure sensor records altitude of rocket at all times
  Advanced altimeters will have additional features - accelerometer
Altimeter's ‘trigger’ your ejection events (black powder charges) for parachute deployment in a dual deployment configuration
  Altimeters are also needed to record your flight apogee

## Slide 5: COTS Altimeter
Altimeters usually contain a drogue and a main channel
  We suggest redundant (aka backup) altimeter / circuit
You will program your altimeters to trigger / deploy your parachutes at certain events
  Ensure you understand the GUI for your altimeter
Your mentor will provide / instruct / assist you with connecting your ejection charges pre-flight
You should test your altimeters in a vacuum chamber

## Slide 6: COTS Altimeter - Simple
May be used as
  Single Deployment (Apogee/Main - Only)
  Dual Deployment (Apogee/Drogue and Main)
If Rocket Speed Is Anticipated to Approach/Transition Mach
  Select ONLY Controllers WITH MACH INHIBIT to Prevent Recovery Deployment While Under Thrust
PerfectFlite StratologgerCF
Featherweight Raven 4

## Slide 7: COTS Altimeter - Advanced
May Provide Additional Features
  Barometric Sensor
  Accelerometer (One-axis, Two, Axis, or Three Axis)
  Gyro Sensors (Usually Three-Axis)
  Mach Inhibit a Usual Feature
  Selectable Barometric or Accelerometer/Gyro- Triggered Apogee (Drogue) Deployment
  Main Parachute Deployment by Barometrically-Sensed Altitude
  Extensive Flight Data Recording and Telemetry, as well as tracking in Some Models
AltusMetrum TeleMetrum

## Slide 8: COTS Altimeter - Circuit
An example dual redundant circuits
  Note the independent circuits
  Note the switch locations
Drogue Parachute
Main Parachute

## Slide 9: COTS Altimeter - Brands
Some common brands (not extensive list)
  Featherweight
    https://www.featherweightaltimeters.com/raven-altimeter.html
  Altus Metrum
    https://altusmetrum.org/
  PerfectFlight
  Missileworks
  https://www.nar.org/contest-flying/us-model-rocket-sporting-code/appendix/altimeters-approved-for-contest-use/

## Slide 10: Avionics Switches
Each altimeter must be on an independent circuit
Each altimeter must have an externally accessible switch
  Your altimeters cannot be turned on until the rocket is vertical on the pad
  The switch is typically accessible on the ‘switch band’ which also contains your vent holes

## Slide 11: Avionics Switches
Considerations
  Use Switches Resistant To Changing States Under G-Forces (+ OR -)
  Don't Rely On Twisted Wires to Complete Circuit
  Screw-Down Switch / Magnetic-Activated Switches Preferred
  Avoid BAT-HANDLE, TOGGLE, and SLIDE Switches
    They Can (And HAVE) Changed State In-Flight, Resulting in Loss of Vehicle
Featherweight Screw Switch
Featherweight Magnetic Switch
MissileWorks 6-32 Screw Switch

## Slide 12: Avionics - Power
Each altimeter must have a dedicated power source
  Power is not shared to other devices
Understand power source your altimeter requires
  They are not all the same (voltage range, current)
Secure your power source for high-G loading
Notes: **insert 9 V and LiPo power source images

## Slide 13: Avionics - Tracking
Your rocket is required to have a tracking device
  *Aside from the Challenge tracking in Moon Challenge
There are a variety of simple plug and play GPS tracking devices offered by the altimeter companies mentioned previously
Ensure you test your tracking device and understand its operation thoroughly

## Slide 14: Avionics - Tracking
Radio Frequency Considerations
  License-Free Operation
  Amateur Band Operation
Components
  Flight Segment
  Ground Segment

## Slide 15: Avionics - Tracking
Radio Tracking Frequency Considerations
  License-Free / Unlicensed Operation
    ISM Band (Industrial, Scientific & Medical)
    315 MHz, 915 MHz, & 2.4GHz in the United States
  Amateur Band Operation
    Requires US Amateur Radio Operator's License
      Technician Class at a Minimum
FNL suggests a license-free tracker and prohibits transmissions that exceed 250 mW.

## Slide 16: Avionics - Tracking

## Slide 17: Avionics - Tracking
Flight Component
  GPS & Antenna
  Tracker Transmitter
  Battery / Power
  Switch
Featherweight GPS
Apogee Simple GPS
AltusMetrum TeleGPS

## Slide 18: Avionics - Tracking
Ground Component
  Receiving Antenna
  Receiver
  Computer or Tablet/ Cellphone
  Software Application Compatible with Tracker and Computer/Cellphone
Apogee Simple GPS
AltusMetrum TeleBT
Featherweight GPS and App

## Slide 19: Avionics – Tracking Brands
Common GPS Trackers (not extensive list)
  Featherweight
    https://www.featherweightaltimeters.com/featherweight-gps-tracker1.html
  Altus Metrum
    https://altusmetrum.org/
  Apogee Components
    https://www.apogeerockets.com/Electronics-Payloads/Rocket-Locators/Simple-GPS-Tracker
There also exist RF tracking options

## Slide 20: Avionics Bay - Hardware
Avionics bay is typically located in the coupler section between the booster and sustainer section
  This means it is located between the drogue parachute (booster) and the main parachute (sustainer) as well

## Slide 21: Avionics Bay - Hardware
Your avionics sled will sit inside the coupler
  You may fabricate your sled to integrate
Your switch / vent band will be centered outside the coupler

## Slide 22: Avionics Hardware - Sleds

## Slide 23: Avionics Hardware – Printed Sleds

## Slide 24: Avionics Bay - Hardware
Mounting Considerations
  Tracking /Telemetry Require RF-Transparent Airframe in Vicinity of Antennas
    No Carbon Fiber
    No Metal (Aluminum, Steel, etc.)
    No Metallic-Finish (Paint, Heat-shrink Covering, etc.)
  Barometric Sensors Require Free Airflow to Operate
    Add Ports/Vent Holes Into Avionics Bay/Switch Band
      See Handbook of Modern Rocketry (G. Harry Stine)
      See Modern High Power Rocketry 2 (Mark Canapa)
      See FNL Competition Handbook

## Slide 25: Avionics Bay - Hardware
Mounting Considerations
  Rigidly Mount All Avionics With Appropriate Hardware to Insure Proper Function
    Accelerometers and Gyros Require Solid Mounting For Error-Free Performance
    All Wiring Should Be Soldered AND/OR Crimped to Insure Connections Under G’s
    Ensure to use the proper size of wiring (based on current / resistance)

## Slide 26: Avionics Bay - Hardware

## Slide 27: Avionics Bay - Hardware

## Slide 28: Avionics Summary
Select Appropriate Avionics to Meet Mission Goals
  Mount Avionics to Prevent Unintended Operation
    Ensure RF-transparent Airframe for Telemetry and Tracking
    Make Secure Electrical Connections
    Allow for Airflow to Barometric Sensors
    Consider REDUNDANT Flight Controllers- More Reliable than a Single Controller!
    Time-Phase Redundant Charge to Fire AFTER Primary Charge by Time or Altitude
    Test What You Will Fly, and Fly ONLY What You Test
    Ensure Deployment Charges are Adequate to Deploy Drogue & Main Parachutes

## Slide 29
Questions?